## Slide 1: Introduction to CUDA
Muhammad Usman
GCUF

## Slide 3
GPUs deliver hundreds GFLOPS on compiled parallel C applications
  Available in laptops, desktops, and clusters
GPU parallelism is doubling every year
Programming model scales transparently
  Data parallelism
Programmable in C with CUDA tools
Multithreaded SPMD model uses application data parallelism and thread parallelism.
[SPMD = Single Program Multiple Data]

## Slide 5
Introduced in 2007 with NVIDIA Tesla architecture
“C-like” language to express programs that run on GPUs using the compute-mode hardware interface
Relatively low-level: CUDA’s abstractions closely match the capabilities/performance characteristics of modern GPUs (low abstraction distance)
Note: OpenCL is an open standards version of CUDA
  CUDA only runs on NVIDIA GPUs
  OpenCL runs on CPUs and GPUs from many vendors

## Slide 6
Compute Unified Device Architecture
Integrated host+device app C program
  Serial or modestly parallel parts in host C code
  Highly parallel parts in device SPMD kernel C code

## Slide 7
A CUDA kernel is executed by an array of threads
  All threads run the same code (the SP in SPMD)
  Each thread has an ID that it uses to compute memory
addresses and make control decisions

## Slide 8
Divide monolithic thread array into multiple blocks
  Threads within a block cooperate via shared memory, atomic operations and barrier synchronization, ...
  Threads in different blocks cannot cooperate

## Slide 15
In CUDA, host and devices have separate memory spaces.
  But in recent GPUs we have Unified Memory Access (UMA)
If GPU and CPU are on the same chip, then they share memory space  fusion

## Slide 20
Almost all API calls return success or failure.
The type of the outcome is: cudError_t
Success  cudaSuccess
Translate the error code to an error message: char * cudaGetErrorString (cudaError_t error)

## Slide 22
int vecAdd(float* A, float* B, float* C, int n)
{
// A_d, B_d, C_d allocations and copies omitted
// Run ceil(n/256) blocks of 256 threads each
vecAddKernel<<<ceil(n/256),256>>>(A_d, B_d, C_d, n);
}
// Each thread performs one pair-wise addition
global
void vecAddkernel(float* A_d, float* B_d, float* C_d, int n)
{
int i = threadIdx.x + blockDim.x * blockIdx.x; if(i<n) C_d[i] = A_d[i] + B_d[i];
}

## Slide 26
int main(void){
// 1: Allocate and initialize the matrices M, N and P
// I/O to read the input matrices M and N
…
// 2: Perform Matrix Multiplication MatrixMultOnHost(M, N, P, Width)
…
// 3: I/O to write the output matrix P
// Free matrices M, N, P
…
return 0;
}

## Slide 28
void MatrixMultiplication (float *M, float *N, float *P, int Width) { int size = Width * Width * sizeof(float);
float *Md, Nd, Pd;
// 1: Transfer M and N to device memory
cudaMalloc((void**), &Md, size);
cudaMemcpy(Md, M, size, cudaMemcpyHostToDevice);
cudaMalloc((void**), &Nd, size);
cudaMemcpy(Nd, N, size, cudaMemcpyHostToDevice);
// Allocate P on the device cudaMalloc((void**), &Pd, size);
// 2: Kernel invocation code -- to be shown later
// 3: Transfer P from device to host
cudaMemcpy(P, Pd, size, cudaMemcpyDeviceToHost);
// Free device matrices
cudaFree(Md); cudaFree(Nd); cudaFree(Pd);
}

## Slide 29
// Matrix multiplication kernel - thread specification
global void MatrixMulKernel(float *Md, float *Nd, float *Pd, int Width)
{
// 2D Thread ID
int tx = threadIdx.x; int ty = threadIdx.y;
//Pvalue stores the Pd element that is computed by the thread
float Pvalue = 0;
for(int k = 0; k < Width; ++k) {
float Mdelement = Md[ty * Width + k] float Ndelement = Nd[k * Width + tx]
Pvalue += Mdelement * Ndelement;
}
// Write the matrix to device memory & each thread writes one element
Pd[ty * Width + tx] = Pvalue;
}

## Slide 30
// Setup the execution configuration
dim3 dimGrid(x, y, z);
dim3 dimBlock(x, y, z);
// Launch the device computation threads!
MatrixMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd, Width);
Important:
dimGrid and dimBlock are user defined
gridDim and blockDim are built-in predefined variables accessible in kernel functions

## Slide 31
Maximum dimensions of a block
Maximum number of threads per block
Maximum dimensions of a grid
Maximum number of blocks per grid

## Slide 33
Data parallelism is the main source of scalability for parallel programs
Each CUDA source file can have a mixture of both host and device code.
What we learned today about CUDA:
  KernelA<<< nBlk, nTid >>>(args)
  cudaMalloc()
  cudaFree()
  cudaMemcpy()
  gridDim and blockDim
  threadIdx and blockIdx
  dim3